## Slide 1: Mobility
Alex Mariakakis
University of Toronto
Department of Computer Science

## Slide 2: Why Care About Mobility?
Leverage trends across communities to understand population-level trends
Urban mobility and access to green space
Epidemic monitoring and contact tracing
Community-level predictors of long-term health

## Slide 3: How Can We Get Mobility Information?
Cell tower triangulation
  Distance from single tower is calculated using signal strength and round-trip time (RTT)
  One tower will get your rough location within a “sector”
  Three towers needed for precise location
Often a combination of triangulation (using angles) and trilateration (using distances)

## Slide 4: How Can We Get Mobility Information?
GPS
  Similar to cell tower triangulation
  Requires four satellites to calculate (x, y, z, time)

## Slide 5: What About Indoors?
Typical accuracy is 5–30 meters
Distance measurements using wireless signals assume line-of-sight
Lots of environmental obstructions from trees, buildings, etc.
Obstructions → poor signal strength → inaccurate distance measurements
Indoor localization is a task of its own

## Slide 6: How Can We Get Mobility Information?
Wi-Fi
  Wi-Fi access points are used to locate devices
    Trilateration: Distance-based measurements
    Fingerprinting: Each location has a signature of nearby access points and signal strengths
  Devices are used to locate Wi-Fi access points
    Companies like Google and Apple maintain tables that map Wi-Fi networks to locations

## Slide 7: Privacy Considerations
Location data is used by many government agencies and companies (ideally de-identified)
De-identification is often not enough

## Slide 8: Resources
Cell Tower Triangulation (GPYes ‘23)
We Tested Mobile GPS/GNSS Accuracy and Found Some Surprising Results (!important Safety Technologies)
Privacy and Data-Based Research (Heffetz and Ligett ‘13)